# CONNECTICUT DEPARTMENT OF ENERGY & ENVIRONMENTAL PROTECTION

MODEL FLOODPLAIN MANAGEMENT REGULATIONS NATIONAL FLOOD INSURANCE PROGRAM (NFIP)

#### Inland/Riverine Community (AE and A Zones only)

#### Level “D” Community

#### October 2018

Please Note:  Effective October 1, 2018, the Connecticut Office of the State Building Inspector (OSBI) amended the current state building code to adopt the 2015 International Residential Code (IRC).  Please see the OSBI website for more information on this change, which can be found at:  https://portal.ct.gov/DAS/Office-of-State-Building-Inspector/Building-and-Fire-Code-Adoption-Process and the 2015 IRC, Chapter 3, Section R322, Flood-Resistant Construction: https://codes.iccsafe.org/public/document/toc/553/.

The adoption of the 2015 IRC has made significant changes to the elevation and construction requirements for new construction and substantially improved structures in both coastal and inland floodplains.  Section R322.2 contains the elevation requirements for A and AE Zones.  Section R322.3 contains the elevation requirements for VE Zones and Coastal AE Zones.  Below is a summary of these new requirements:

- AE and A Zone – Lowest floor elevated to Base Flood Elevation (BFE) plus 1 	foot.

- AO and AH Zones – Lowest floor elevated to Highest Adjacent Grade (HAG) as 	the depth number specified on the flood insurance rate map plus 1 foot or not 	less than 3 feet if no depth number is specified.

- VE Zone and Coastal AE Zone – Bottom of the lowest horizontal member 	supporting the lowest floor elevated to the BFE plus one foot, with structure built 	on pier, post or pile foundation utilizing breakaway walls.  Breakaway walls in 	Coastal AE zones must also contain hydraulic flood vents.

The adoption of the 2015 IRC will make significant changes to the elevation requirement for new construction and substantially improved structures in coastal floodplains that may be different than the standards currently contained in your local floodplain zoning regulations or ordinance.  There are also other changes.  Bold red text in this model highlights the changes that need to be made to floodplain zoning regulations or ordinances to match the new state building code standards.

###### TABLE OF CONTENTS

- Statutory Authorization and Purpose

  - Statutory Authorization

  - Finding of Fact

  - Statement of Purpose

  - Objectives

- Definitions

- General Provisions

  - Areas to Which This [Ordinance/Regulation] Applies

  - Basis for Establishing the Special Flood Hazard Areas (SFHA)

  - Structures Already in Compliance

  - Abrogation and Greater Restrictions

  - Interpretation

  - Warning and Disclaimer of Liability

  - Severability

- Administration

  - Designation of the Local Administrator

  - Certification

  - Establishment of the Floodplain Development Permit

OR

Establishment of the Flood Management Section of the                                                        [Development/Building/Zoning] Permit

  - Permit Application Procedures

    - Application Stage

    - Construction Stage

  - Duties and Responsibilities of the Local Administrator

- Provisions for Flood Hazard Reduction

  - General Standards

  - Standards for Watercourses Without BFEs, Floodways and/or Flood Mapping

  - Specific Standards

    - Construction Standards in Special Flood Hazard Areas (SFHA), Zones A, A1-30, and AE

    - Manufactured (Mobile) Homes and Recreational Vehicles (RVs)

    - Floodways

    - Standards for Development in Areas of Shallow Flooding (AO and AH Zones)

- Design Standards for Subdivision Proposals

- Variance Procedures

  - Establishment of Variance Process

  - Specific Situation Variances

  - Considerations for Granting of Variances

  - Conditions for Variances

- Enforcement

- Penalties for Violation

NOTES:

Text in italics is for information purposes only and can be deleted.

Text that is bolded and in brackets, [bold text], must be completed by the community and unbolded.

- STATUTORY AUTHORIZATION AND PURPOSE

1.1     STATUTORY AUTHORIZATION

The Legislature of the State of Connecticut has in Title 7, Chapter 98, Section 7-148(c)(7)(A) and in Title 8, Chapter 124, Section 8-2 of the General Statutes delegated the responsibility to local governmental units to adopt regulations designed to promote the public health, safety, and general welfare of its citizenry.  Therefore, the [Governing Body] of the [Municipality], Connecticut, does ordain as follows:

# 1.2	FINDING OF FACT

The flood hazard areas of the [Municipality] are subject to periodic flood inundation which results in the loss of life and property, health and safety hazards, disruption of commerce and governmental services, extraordinary public expenditures for flood protection and relief, and impairment of the tax base, all of which adversely affect the public health, safety and general welfare.

These flood losses are caused by the cumulative effect of obstructions in the floodplains causing increases in flood heights and velocities, and by the occupancy in flood hazard areas by uses vulnerable to floods or hazards to other lands which are inadequately elevated, floodproofed, or otherwise unprotected from flood damage.  Uncontrolled development and use of the floodplains can adversely affect the community.

The [Municipality] has voluntarily participated in the National Flood Insurance Program (NFIP)       since [date of entry into the regular program].  The NFIP is founded on a mutual agreement           between the federal government and each participating community.  Local, state and federal               governments must share roles and responsibilities to meet the goals and objectives of the NFIP.          The community’s role is of paramount importance.  Property owners are able to receive federally-      subsidized flood insurance only if the community enacts and enforces the minimum floodplain           regulations required for participation in the NFIP.

# 1.3	STATEMENT OF PURPOSE

It is the purpose of this [ordinance/regulation] to regulate floodplain development, promote public health, safety, and general welfare, and minimize public and private losses due to flood conditions in specific areas by provisions designed to:

1.3.1 	To protect human life and health, and prevent damage to property;

1.3.2 	To minimize expenditure of public funds for costly flood control projects;

1.3.3 	To minimize the need for rescue and relief efforts associated with flooding and generally undertaken at the expense of the general public;

1.3.4 	To minimize prolonged business interruptions and other economic disruptions;

1.3.5 	To minimize damage to public facilities, infrastructure and utilities, such as water and gas mains, electric, telephone and sewer lines, and streets and bridges, located in the floodplain;

1.3.6   To help maintain a stable tax base by providing for the sound use and development of flood

hazard areas in such a manner as to minimize flood damage and flood blight areas;

    - To insure that potential buyers are notified that property is in a flood hazard area;

    - To prevent increase in flood heights that could increase flood damage and result in conflicts between property owners;

    - To ensure that those who occupy the flood hazard areas assume responsibility for their actions; and

    - To discourage development in a floodplain if there is any practicable alternative to locate the activity, use or structure outside of the floodplain.

  - OBJECTIVES

In order to accomplish its purposes, this [ordinance/regulation] includes objectives, methods and            provisions that:

1.4.1 	Restrict or prohibit uses which are dangerous to health, safety and property due to flood                            or erosion hazards, or which result in damaging increases in erosion or in flood heights or                         velocities;

1.4.2 	Require that uses vulnerable to floods, including facilities that serve such uses, be protected            against flood damage at the time of initial construction;

1.4.3 	Control the alteration of natural floodplains, stream channels, and natural protective                        barriers that are involved in the accommodation of flood waters;

1.4.4 	Control filling, grading, dredging and other development which may increase erosion or                 flood damage; and

1.4.5 	Prevent or regulate the construction of barriers or obstructions which will unnaturally divert            flood waters or which may increase flood hazards to other lands.

# 2.0	DEFINITIONS

Unless specifically defined below, words and phrases used in this [ordinance/regulation] shall have the same meaning as they have in common usage and to give this [ordinance/regulation] its most reasonable application.

Area of Shallow Flooding (for a community with AO or AH Zones only) - A designated AO, AH, AR/AO, AR/AH, or VO zone on a community’s Flood Insurance Rate Map (FIRM) with a one percent or greater annual chance of flooding to an average depth of one to three feet where a clearly defined channel does not exist, where the path of flooding is unpredictable, and where velocity flow may be evident.  Such flooding is characterized by ponding or sheet flow.

Base Flood – The flood having a one (1) percent chance of being equaled or exceeded in any given           year, also referred to as the one hundred (100) year flood, as published by the Federal Emergency             Management Agency (FEMA) as part of a Flood Insurance Study (FIS) and depicted on a Flood               Insurance Rate Map (FIRM).

Base Flood Elevation (BFE) – The elevation of the crest of the base flood or 100-year flood.                   The height in relation to mean sea level expected to be reached by the waters of the base flood at              pertinent points in the floodplains of coastal and riverine areas.

Basement – Any area of the building having its floor subgrade (below ground level) on all sides.

Building – see definition for “Structure”.

Cost  (optional definition, but recommended, relates to substantial improvement)  – As related to substantial improvements, the cost of any reconstruction, rehabilitation, addition, alteration, repair or other improvement of a structure shall be established by a detailed written contractor’s estimate.  The estimate shall include, but not be limited to:  the cost of materials (interior finishing elements, structural elements, utility and service equipment); sales tax on materials, building equipment and fixtures, including heating and air conditioning and utility meters; labor; built-in appliances; demolition and site preparation; repairs made to damaged parts of the building worked on at the same time; contractor’s overhead; contractor’s profit; and grand total.  Items to be excluded include:  cost of plans and specifications, survey costs, permit fees, outside improvements such as septic systems, water supply wells, landscaping, sidewalks, fences, yard lights, irrigation systems, and detached structures such as garages, sheds, and gazebos.

Development – Any man-made change to improved or unimproved real estate, including but not limited to the construction of buildings or structures; the construction of additions, alterations or substantial improvements to buildings or structures; the placement of buildings or structures; mining, dredging, filling, grading, paving, excavation or drilling operations or storage of equipment; the storage, deposition, or extraction of materials; and the installation, repair or removal of public or private sewage disposal systems or water supply facilities.

Existing Manufactured Home Park or Subdivision – A manufactured home park or subdivision for which the construction of facilities for servicing the lots on which the manufactured home are   to be affixed (including, as a minimum, the installation of utilities, the construction of streets, and  either final site grading or the pouring of concrete pads) is completed before [effective date of floodplain regulations or ordinance], the effective date of the floodplain management regulations adopted by the community.

Expansion to an Existing Manufactured Home Park or Subdivision – The preparation of                    additional sites by the construction of facilities for servicing the lots on which the manufacturing              homes are to be affixed (including the installation of utilities, the construction of streets, and either           final site grading or the pouring of concrete pads).

Federal Emergency Management Agency (FEMA) - The federal agency that administers the National Flood Insurance Program (NFIP).

Finished Living Space (optional definition, include only if used in regulation language for fully enclosed areas below BFE)  – As related to fully enclosed areas below the base flood elevation (BFE), a space that is, but is not limited to, heated and/or cooled, contains finished floors, has sheetrock walls that may or may not be painted or wallpapered, and other amenities such as furniture, appliances, bathrooms, fireplaces and other items that are easily damaged by floodwaters and expensive to clean, repair or replace.  Unfinished enclosed areas below the BFE should comply with FEMA Technical Bulletin 2, Flood-Damage Resistant Materials Requirements.

Flood or Flooding – A general and temporary condition of partial or complete inundation of normally dry land areas from either the overflow of inland or tidal waters, or the unusual and rapid accumulation/runoff of surface waters from any source.

Flood Insurance Rate Map (FIRM) – The official map of a community on which the Federal Emergency Management Agency (FEMA) has delineated both the special flood hazard areas (100-year floodplain) and the insurance risk premium zones applicable to a community.

Flood Insurance Study (FIS) – The official study of a community in which the Federal Emergency Management Agency (FEMA) has conducted an examination, evaluation and determination of flood hazards and, if appropriate, corresponding water surface elevations.

Floodway – The channel of a river or other watercourse and the adjacent land areas that must be reserved in order to discharge the base flood without cumulatively increasing the water surface elevation more than one (1.0) foot.  For the purposes of these regulations, the term “Regulatory Floodway” is synonymous in meaning with the term “Floodway”.

Functionally Dependent Use or Facility – A use or facility that cannot perform its intended purpose unless it is located or carried out in close proximity to water.  The term includes only docking facilities, port facilities that are necessary for the loading and unloading of cargo or passengers, and ship building and ship repair facilities.  The term does not include seafood processing facilities, long-term storage, manufacturing, sales or service facilities.

Highest Adjacent Grade (HAG) (for community with AO/AH zones) – The highest natural elevation of the ground surface prior to construction next to the proposed walls of a structure.

Historic Structure – Any structure that is:  (a) Listed individually in the National Register of Historic Places (a listing maintained by the Department of the Interior) or preliminarily determined by the Secretary of the Interior as meeting the requirements for individual listing on the National Register; (b) Certified or preliminarily determined by the Secretary of the Interior as contributing to the historic significance of a registered historic district or a district preliminarily determined by the Secretary to qualify as a registered historic district; (c) Individually listed on a state inventory of historic places in states with historic preservation programs which have been approved by the Secretary of the Interior; or (d) Individually listed on a local inventory of historic places in communities with historic preservation programs that have been certified either:  (1) By an approved state program as determined by the Secretary of the Interior or (2) Directly by the Secretary of the Interior in states without approved programs.

Lowest Floor – The lowest floor of the lowest enclosed area (including basement).  An unfinished or flood resistant enclosure, usable solely for parking of vehicles, building access or storage, in an area other than a basement area is not considered a building’s lowest floor, provided that such an area meets the design requirements specified in Section 5.3.1.3 of this [ordinance or regulation].

Manufactured Home – A structure, transportable in one (1) or more sections, which is built on a permanent chassis and is designed for use with or without a permanent foundation when attached to the required utilities.  The term also includes park trailers, travel trailers, recreational vehicles and other similar vehicles or transportable structures placed on a site for one hundred and eighty (180) consecutive days or longer and intended to be improved property.

Manufactured Home Park or Subdivision – A parcel or contiguous parcels of land divided into two (2) or more manufactured home lots for rent or sale.

Market Value – As related to substantial improvement and substantial damage, the market value of the structure shall be determined by (choose one of the following:  an independent appraisal by a professional appraiser; the property’s tax assessment, minus land value; the replacement cost minus depreciation of the structure; the structure’s Actual Cash Value) prior to the start of the initial repair or improvement, or in the case of damage, the value of the structure prior to the damage occurring.

Mean Sea Level (MSL) – The North American Vertical Datum (NAVD) of 1988 or other datum, to which base flood elevations shown on a community’s Flood Insurance Rate Map (FIRM) are referenced.

New Construction – Structures for which the “start of construction” commenced on or after [effective date of floodplain regulations, date of initial adoption], the effective date of the floodplain management regulations, and includes any subsequent improvements to such structures.

New Manufactured Home Park or Subdivision – A manufactured home park or subdivision for which the construction of facilities for servicing the lots on which the manufactured homes are to be affixed (including at a minimum, the installation of utilities, the construction of streets, and either final site grading or the pouring of concrete pads) is completed on or after [effective date of floodplain regulations or ordinance], the effective date of the floodplain management regulation adopted by the community.

Recreational Vehicle – A vehicle which is:  (a) built on a single chassis; (b) four hundred (400) square feet or less when measured at the largest horizontal projection; (c) designed to be self-propelled or permanently towable by a light duty truck; and (d) designed primarily not for use as a permanent dwelling but as a temporary living quarters for recreational, camping, travel, or seasonal use.

Special Flood Hazard Area (SFHA) – The land in the floodplain within a community subject to a one (1) percent or greater chance of flooding in any given year.  SFHAs are determined utilizing the base flood elevations (BFE) provided on the flood profiles in the Flood Insurance Study (FIS) for a community.  BFEs provided on Flood Insurance Rate Map (FIRM) are only approximate (rounded up or down) and should be verified with the BFEs published in the FIS for a specific location.  SFHAs include, but are not necessarily limited to, the land shown as Zones A, A1-30, AE, AO, AH on a FIRM.  The SFHA is also called the Area of Special Flood Hazard.

Start of Construction – For other than new construction or substantial improvements under the Coastal Barrier Resources Act (P.L. 97-348), includes substantial improvement and means the date the building permit was issued, provided the actual start of construction, repair, reconstruction, rehabilitation, addition placement, substantial improvement or other improvement was within one hundred and eighty (180) days of the permit date.  The actual start means either the first placement of permanent construction of a structure on a site, such as the pouring of slab or footings, the installation of piles, the construction of columns, or any work beyond the stage of excavation, or the placement of a manufactured home on a foundation.  Permanent construction does not include land preparation, such as clearing, grading and filling; nor does it include the installation of streets and/or walkways; nor does in include excavation for a basement, footings, piers, or foundations or the erections of temporary forms; not does it include the installation on the property of accessory buildings, such as garages or sheds not occupied as dwelling units or not part of the main structure.  For a substantial improvement, the actual start of construction means the first alteration of any wall, ceiling, floor, or other structural part of a building, whether or not that alteration affects the external dimensions of the building.

Structure – A walled and roofed building which is principally above ground, including a manufactured home, a gas or liquid storage tank, or other man-made facilities or infrastructures.

Substantial Damage – Damage of any origin sustained by a structure, whereby the cost of restoring the structure to its pre-damaged condition would equal or exceed 50 percent of the market value of the structure before the damage occurred.

Substantial Improvement – Any combination of repairs, reconstruction, rehabilitation, alterations, additions or other improvements to a structure, taking place during a ten (10) year period, in which the cumulative cost equals or exceeds fifty (50) percent of the market value of the structure before the “start of construction” of the improvement.  This term includes structures that have incurred “substantial damage”, regardless of the actual repair work performed. For purposes of this definition, “substantial improvement” is considered to occur when the first alteration of any wall, ceiling, floor, or other structural part of the building commences, whether or not that alteration affects the external dimensions of the structure.  The term does not, however, include either:  (1) Any project for improvement of a structure to correct existing violations of state or local health, sanitary, or safety code specifications which have been identified by the local code enforcement official and which are the minimum necessary to assure safe living conditions; or (2) Any alteration of a “historic structure”, provided that the alteration will not preclude the structure’s continued designation as a “historic structure”.

Variance - A grant of relief by a community from the terms of the floodplain management [ordinance/regulation] that allows construction in a manner otherwise prohibited and where specific enforcement would result in unnecessary hardship.

Violation – Failure of a structure or other development to be fully compliant with the community’s floodplain management [ordinance/regulations].  A structure or other development without required permits, lowest floor elevation documentation, flood-proofing certificates or required floodway encroachment calculations is presumed to be in violation until such time as that documentation is provided.

Water Surface Elevation – The height, in relation to the North American Vertical Datum (NAVD) of 1988 (or other datum, where specified), of floods of various magnitudes and frequencies in the floodplains of coastal or riverine areas.

# 3.0	GENERAL PROVISIONS

# 3.1	AREAS TO WHICH THIS [ORDINANCE/REGULATION] APPLIES

This [ordinance/regulation] shall apply to all Special Flood Hazard Areas (SFHA) within the

[Municipality].

3.2	BASIS FOR ESTABLISHING THE SPECIAL FLOOD HAZARD AREAS (SFHA)

The Special Flood Hazard Areas (SFHA) identified by the Federal Emergency Management

Agency (FEMA) in its Flood Insurance Study (FIS) for [County], dated [date of most recent

FIS], accompanying Flood Insurance Rate Maps (FIRM), dated [date of most recent FIRM],

and other supporting data applicable to the [Municipality], and any subsequent revisions

thereto, are adopted by reference and declared to be a part of this [ordinance/regulation].	Since

mapping is legally adopted by reference into this [ordinance/regulation] it must take precedence

when more restrictive until such time as a map 	amendment or map revision is obtained from

FEMA.

The SFHA includes any area shown on the FIRM as Zones A, AE, AO, and AH, including

areas designated as a floodway on a FIRM.  SFHAs are determined utilizing the base

flood elevations (BFE) provided on the flood profiles in the Flood Insurance Study (FIS) for a

community.  BFEs provided on Flood Insurance Rate Map (FIRM) are only approximate (rounded

up or down) and should be verified with the BFEs published in the FIS for a specific location.

Also included are areas of potential, demonstrable or historical flooding, including any area

contiguous with but outside the SFHA identified by FEMA, and where the land surface elevation is

lower than the base flood elevation (BFE) as shown in the FIS, and the area is not protected from

flooding by a natural or man-made feature.  The FIRM and FIS are on file in the

[Municipal Office], [Office Location], [Municipality].

3.3    STRUCTURES ALREADY IN COMPLIANCE

A structure or development already in compliance with this [ordinance/regulation] shall not be

made non-compliant by any alteration, modification, repair, reconstruction or improvement and

must also comply with other applicable local, state, and federal regulations.  No structure or land

shall hereafter be located, extended, converted, modified or structurally altered without full

compliance with the terms of this [ordinance/regulation] and other applicable regulations.

3.4	ABROGATION AND GREATER RESTRICTIONS

This [ordinance/regulation] is not intended to repeal, abrogate or impair any existing easements,

covenants, or deed restrictions.  However, where this [ordinance/regulation] and another

ordinance, regulation easement, covenant or deed restriction conflict or overlap, whichever

imposes the more stringent restrictions shall prevail.

# 3.5     INTERPRETATION

In the interpretation and application of this [ordinance/regulation], all provisions shall be: 1) considered as minimum requirements; 2) liberally construed in favor of the governing body, and; 3) deemed neither to limit nor repeal any other powers granted under State statutes.

# 3.6  	WARNING AND DISCLAIMER OF LIABILITY

The degree of flood protection required by this [ordinance/regulation] is considered the

minimum reasonable for regulatory purposes and is based on scientific and engineering

consideration and research.  Larger floods can and will occur on rare occasions.  Flood heights

may be increased by man-made or natural causes.  This [ordinance/regulation] does not imply or

guarantee that land outside the Special Flood Hazard Area or uses permitted in such areas will be

free from flooding and flood damages. This [ordinance/regulation] shall not create liability on

the part of the [Municipality] or by any officer or employee thereof for any flood damages that

result from reliance on this [ordinance/regulation] or any administrative decision lawfully made

thereunder.	The [Municipality], its officers and employees shall assume no liability for another

person’s reliance on any maps, data or information provided by the [Municipality].

# 3.7	SEVERABILITY

If any section, subsection, paragraph, sentence, clause, or phrase of this [ordinance/regulation]

should be declared invalid for any reason whatsoever, such decision shall not affect the remaining

portions of this [ordinance/regulation], which shall remain in full force and effect; and to this

end the provisions of this [ordinance/regulation] are hereby declared to be severable.

# 4.0  	ADMINISTRATION

# 4.1  	DESIGNATION OF THE LOCAL ADMINISTRATOR

The [title of local administrator] is hereby appointed to administer, implement and enforce the

provisions of this [ordinance/regulation].

4.2	CERTIFICATION

# Where required under this [ordinance/regulation], a registered professional engineer or architect shall certify that the design and methods of construction are in accordance with accepted standards of practice for meeting the provisions of this [ordinance/regulation].  Such certification must be provided to the [title of local administrator].

# 4.3	ESTABLISHMENT OF THE FLOODPLAIN DEVELOPMENT PERMIT

A Floodplain Development Permit shall be required in conformance with the provisions of this

[ordinance/regulation] prior to the commencement of any development activities.  Permits issued

under this [ordinance/regulation] shall expire if actual construction of a permitted structure does

not commence within one hundred and eighty (180) days of the permit approval date.

OR

ESTABLISHMENT OF THE FLOOD MANAGEMENT SECTION OF THE                                     [DEVELOPMENT/BUILDING/ZONING] PERMIT

The flood management section of the [Development/Building/Zoning] Permit must be

completed in conformance with the provisions of this [ordinance/regulation] prior to the commencement of any development activities.  Permits issued under this [ordinance/regulation] shall expire if actual construction of a permitted structure does not commence within one hundred and eighty (180) days of the permit approval date.

# 4.4 	PERMIT APPLICATION PROCEDURES

A [floodplain development/development/building/zoning] permit is hereby established for all construction and other development to be undertaken in Special Flood Hazard Areas in this community.  Prior to any development activities, application for a [floodplain development/development/building/zoning] permit shall be made to the [title of local administrator] on forms provided and may include, but not be limited to, plans in duplicate drawn to scale showing, at a minimum, the property lines and location of the parcel; the nature, location, dimensions, and elevations of the area in question; limit and extent of the 100-year floodplain and/or floodway boundary and base flood elevation(s); existing and proposed structures, fill, storage of materials, drainage facilities and the location of the foregoing. Specifically, the following information is required to be submitted to the [title of local administrator]:

    - Application Stage

The applicant shall provide at least the following information, where applicable.  Additional                       information may be required on the permit application form.

4.4.1.1  Base flood elevation (BFE) for the site in question as determined in the FEMA

Flood Insurance Study (FIS) or Flood Insurance Rate Map (FIRM).  The FIS flood    profiles provide more accurate BFE data than the FIRM.  The extent of the 100-        year floodplain and floodway must be depicted with a boundary line on any site         plans and shown in relation to existing and proposed structures or development;

4.4.1.2  Elevation in relation to mean sea level of the proposed lowest floor,

including basement, of all new construction, substantial improvements or repairs to structures that have sustained substantial damage;

4.4.1.3  Elevation in relation to mean sea level to which any non-residential new                                           construction, substantial improvements or repair to structures that have sustained                            substantial damage will be dry flood-proofed;

      - Description of the extent to which any watercourse will be altered or relocated as a result of the proposed development.  Computations by a registered professional engineer must be submitted that demonstrate that the altered or relocated segment will provide equal or greater conveyance than the original stream segment.  The applicant must submit any maps, computations or other materials required by the Federal Emergency Management Agency (FEMA) in order to officially amend or revise the Flood Insurance Rate Map.  The applicant must pay any fees or other costs assessed by FEMA for this purpose.  The applicant must also provide assurances that the conveyance capacity of the altered or relocated stream segment will be maintained;

4.4.1.5  A statement and supporting documentation (all costs of project, market value of                   structure, etc.) verifying that the proposed alterations to an existing structure meets              or does not meet the criteria of the substantial improvement and/or substantial                      damage definition.  If a development meets the definition of substantial                                improvement and/or substantial damage, the structure must be brought into                            compliance with all floodplain regulations as if it was new construction;

      - Where applicable the following certifications by a registered professional engineer or architect are required, and must be provided to the [title of local administrator].  The design and methods of construction must be certified to be in accordance with accepted standards of practice and with the provisions of Section 5.3.

(a)  Non-residential flood-proofing must meet the provisions of Section 5.3.1.2;

- Fully enclosed areas below the base flood elevation (BFE) must meet the minimum design criteria in Section 5.3.1.3;

- No (0.00) increase in floodway water surface elevations are allowed.  Any development in a floodway must meet the provisions of Section 5.3.4;

    - Construction Stage

Upon completion of the applicable portion of construction, the applicant shall provide                 verification to the [title of local administrator] of the following as is applicable:

4.4.2.1. Lowest floor elevation shall be verified for:

- A structure in Zones A, AE, A1-30, AO or AH is the top of the lowest floor (including basement);

- A non-residential structure which has been dry flood-proofed is the elevation to which the flood-proofing is effective (Note:  For insurance purposes, a dry flood-proofed, non-residential structure is rated based on the elevation of its lowest floor unless it is floodproofed to one foot above the BFE.);

4.4.2.2 Deficiencies detected by the review of the above listed shall be corrected by the                                         permit holder immediately and prior to further progressive work being permitted                                        to proceed.  Failure to submit the survey or failure to make said corrections                                                required hereby, shall be cause to issue a stop-work order for the project.

# 4.5	DUTIES AND RESPONSIBILITIES OF THE LOCAL ADMINISTRATOR

# Duties of the [title of local administrator] shall include, but not be limited to:

# 4.5.1 Review all permit applications for completeness, particularly with the requirements of                     Section 4.4.1.

# 4.5.2 Review all permit applications to determine whether the proposed development and building            sites will be reasonably safe from flooding.

# Review all development permits to assure that the permit requirements of this

# [ordinance/regulation] have been satisfied.

# 4.5.4   Review all permit applications to assure that all necessary federal or state permits have                   been received.  Require that copies of such permits be provided and maintained on file with            the permit application.  Such permits include, but are not limited to, Coastal Area                            Management (CAM) Permit, Water Diversion Permit, Dam Safety Permit, and Army Corps            of Engineers 401 and 404 Permits.

# Notify the regional planning agency and affected municipality at least thirty-five (35) days

# prior to a public hearing if any change of regulation or use of a flood zone will affect an                 area within five hundred (500) feet of another municipality.

# 4.5.6	Notify the adjacent communities and the Department of Energy and Environmental 	Protection (DEEP), Inland Water Resources Division, prior to any alteration or relocation              of a watercourse, and submit evidence of such notification to the Federal Emergency                      Management Agency.

# Assure that maintenance is provided within the altered or relocated portion of said

# watercourse so that the flood carrying capacity is not diminished.

# Obtain, record and maintain the elevation (in relation to mean sea level) of the lowest floor (including basement) of all new construction, substantial improvements or repair to a structure that has sustained substantial damage.

# Obtain, record and maintain the elevation (in relation to mean sea level) to which the new construction, substantial improvement or repair to a structure that has sustain substantial damage has been flood-proofed.

# When flood-proofing is utilized for a particular structure, the [title of local administrator]

# shall obtain certification from a registered professional engineer or architect, in accordance

# with Section 5.3.1.2.

# Where interpretation is needed as to the exact location of boundaries of the area of special

# flood hazard (for example, where there appears to be a conflict between a mapped boundary            and actual field conditions) the [title of local administrator] shall make necessary                         interpretation.  The person contesting the location of the boundary shall be given a                          reasonable opportunity to appeal the interpretation as provided in this

# [ordinance/regulation].

# Require the applicant to provide base flood elevation data for all proposed development,

# including manufactured home parks and subdivisions.

# When base flood elevation data or floodway data have not been provided in accordance

# with Section 3.2 and Section 4.4, the [title of local administrator] shall obtain, review and reasonably utilize any base flood elevation and floodway data available from a federal, state or other source in order to administer the provisions of Section 5.0.

# All records pertaining to the provisions of this [ordinance/regulation] shall be obtained

# and maintained in the office of the [title of local administrator].

# Upon completion of the permitted development and prior to issuance of a Certificate of

# Occupancy (CO), necessary as-built surveys (prepared by a Connecticut Licensed                                      Professional as per Connecticut State Statutes) and engineering and architectural                                        certifications shall be provided to the [title of local administrator] demonstrating                                     compliance with the approved plans and standards set forth in Section 4.4.

# 5.0	PROVISIONS FOR FLOOD HAZARD REDUCTION

# 5.1	GENERAL STANDARDS

In all Special Flood Hazard Areas (SFHAs) the following provisions are required:

    - New construction, substantial improvements, and structures that have sustained substantial

damage shall be constructed using methods and practices that minimize flood damage.

5.1.2  New construction, substantial improvements, and structures that have sustained substantial damage shall be constructed with materials and utility equipment that are flood-damage resistant and conform to the provisions of FEMA Technical Bulletin 2, Flood Damage-Resistant Material Requirements.  This includes, but is not limited to, flooring, interior and exterior walls, wall coverings and other materials installed below the base flood elevation plus one (1.0) foot.

5.1.3 New construction, substantial improvements, and repairs to structures that have sustained

substantial damage shall be anchored to prevent flotation, collapse or lateral movement of                         the structure resulting from hydrodynamic and hydrostatic loads, including the effects of                           buoyancy.

5.1.4	New construction, substantial improvements and repair to structures that have sustained substantial damage cannot be constructed or located entirely or partially over water unless they are a functionally dependent use or facility.

5.1.5	The bottom of all electrical, heating, plumbing, ventilation and air conditioning 	equipment, appliances, fixtures and components, HVAC duct work and duct 	systems, and any other utility service equipment, facilities, machinery, or 	connections servicing a structure shall be elevated one (1.0) foot above the base 	flood elevation (BFE).  This includes, but is not limited to, furnaces, oil or propane 	tanks, air conditioners, heat pumps, hot water heaters, ventilation duct work, 	washer and dryer hook-ups, electrical junction boxes, and circuit breaker boxes.  	Systems, fixtures, equipment and components shall not be mounted on or penetrate 	through breakaway walls intended to fail under flood loads.  Connections or other 	equipment that must be located below the BFE plus 1.0 foot elevation are permitted 	only when no other elevation alternative is available and provided they are 	designed and installed to prevent water from entering or accumulating within 	the components and to resist hydrostatic and hydrodynamic 	loads and stresses, 	including the effects of buoyancy, during the occurrence of the base flood event.   	Electrical wiring systems that must be located below the BFE plus 1.0 foot shall 	conform to the standards for wet locations.

5.1.6	 New and replacement water supply systems shall be designed to minimize or eliminate

infiltration of flood waters into the system.

5.1.7   New and replacement sanitary sewage systems shall be designed to minimize or eliminate

infiltration of flood waters into the system and discharges from the system into flood                      waters.

5.1.8   On-site waste disposal systems shall be located and constructed to avoid impairment to

them or contamination from them during flooding.

    - Underground tanks shall be anchored to prevent flotation, collapse and lateral movement under conditions of the base flood.  Above-ground storage tanks which are located outside or inside of a structure must be elevated one (1.0) foot above the base flood elevation (BFE) or shall be securely anchored to prevent flotation, collapse or lateral movement under conditions of the base flood. Where elevated on platforms, the platforms shall be cantilevered from or knee braced to the building or shall be supported on elevated foundations that conform to the standards for the particular flood zone as described in Section 5.3.  Anchored tanks must have the top of the fill pipe located at least one (1.0) foot above the BFE and have a screw fill cap that does not allow for the infiltration of flood water.

5.1.10 In any portion of a watercourse that is altered or relocated, the flood carrying capacity must             be maintained.  Notify adjacent communities and the Connecticut Department of Energy                and Environmental Protection (CTDEEP), Inland Water Resources Division (IWRD) prior             to any alteration or relocation of a watercourse.

5.1.11 If any portion of a structure lies within the Special Flood Hazard Area (SFHA), the                entire structure is considered to be located within the SFHA and must meet the                       construction requirements of the flood zone.  The structure includes any structurally              attached additions, garages, decks, porches, sunrooms, patios or any other structure               attached to the main structure.

5.1.12 If a structure lies within two or more flood zones, the construction standards of the               most restrictive zone apply to the entire structure (i.e., VE zone is more restrictive                 than AE zone; structure must be built to the highest BFE).  The structure includes any           structurally attached additions, garages, decks, porches, patios, sunrooms, or any other          structure attached to the main structure.

5.1.13 Compensatory Storage.  The water holding capacity of the floodplain, except those areas                which are tidally influenced, shall not be reduced.  Any reduction caused by filling, new                 construction or substantial improvements involving an increase in footprint to the                            structure, shall be compensated for by deepening and/or widening of the floodplain.                        Storage shall be provided on-site, unless easements have been gained from adjacent                        property owners; it shall be provided within the same hydraulic reach and a volume not                  previously used for flood storage; it shall be hydraulically comparable and incrementally                equal to the theoretical volume of flood water at each elevation, up to and including the                  100-year flood elevation, which would be displaced by the proposed project.  Such                         compensatory volume shall have an unrestricted hydraulic connection to the same                           waterway or water body.  Compensatory storage can be provided off-site if approved by                 the municipality.

5.1.14 Equal Conveyance.  Within the floodplain, except those areas which are tidally                                    	influenced, as designated on the Flood Insurance Rate Map (FIRM) for the community,                             encroachments resulting from filling, new construction or substantial improvements                                   involving an increase in footprint of the structure, are prohibited unless the applicant                                 provides certification by a registered professional engineer demonstrating, with supporting                        hydrologic and hydraulic analyses performed in accordance with standard engineering                               practice, that such encroachments shall not result in any (0.00 feet) increase in flood levels                        (base flood elevation).  Work within the floodplain and the land adjacent to the floodplain,                        including work to provide compensatory storage shall not be constructed in such a way so                         as to cause an increase in flood stage or flood velocity.

5.2	STANDARDS FOR WATERCOURSES WITHOUT ESTABLISHED BASE FLOOD ELEVATIONS (UN-NUMBERED A ZONE), ADOPTED FLOODWAYS AND/OR FLOOD MAPPING

    - The [title of local administrator] shall require base flood elevation (BFE) data be provided with any application for new construction, substantial improvement, repair to structures which have sustained substantial damage or other development in Zone A without a FEMA-published BFE (un-numbered A Zone).  A registered professional engineer must determine the BFE in accordance with accepted hydrologic and hydraulic engineering practices and document the technical methods used.  Studies, analyses and computations shall be submitted in sufficient detail to allow thorough review and approval.  The [title of local administrator] shall obtain, review and reasonably utilize any BFE and floodway data available from a federal, state or other source, including data developed for subdivision proposals, as criteria for requiring that new construction, substantial improvements, repair to structures which have sustained substantial damage or other development in un-numbered A Zones on the community’s Flood Insurance Rate Map (FIRM) meet the standards in Section 4.4 and Section 5.3.  If no BFE can be determined, the lowest floor, including basement, must be elevated to two (2) feet above the highest adjacent grade next to the structure.

5.2.2	When BFEs have been determined within Zones A1-30 and AE on the community’s FIRM but a regulatory floodway has not been designated, the [title of local administrator] must require that no new construction, substantial improvements, repair to structures which have sustained substantial damage or other development, including fill, shall be permitted which will increase the water surface elevation of the base flood more than one (1.0) foot at any point within the community when all existing and anticipated development is considered cumulatively with the proposed development.

    - The [title of local administrator] may request floodway data of an applicant for

watercourses without FEMA-published floodways.  When such data is provided by an                    applicant or whenever such data is available from any other source (in response to the                     municipality’s request or not), the community shall adopt a regulatory floodway based on               the principle that the floodway must be able to convey the waters of the base flood without             increasing the water surface elevation more than one (1.0) foot at any point within the                    community.

    - The [title of local administrator] shall obtain, review and reasonably utilize any BFE and

floodway data available from a federal, state or other source, as criteria for requiring that                new construction, substantial improvements, repair to structures which have sustained                    substantial damage or other development in any area of potential, demonstrable or historical            flooding within the community meet the standards in Section 4.4 and Section 5.3.

5.2.5	Under the provisions of 44 CFR Chapter 1, Section 65.12, of the National Flood Insurance Program regulations, a community may approve certain development in Zones A1-30, AE, AH, on the community’s FIRM which increases the water surface elevation of the base flood by more than one (1.0) foot, provided that the community first completes all of the provisions required by Section 65.12.

# 5.3	SPECIFIC STANDARDS

    - Construction Standards in Special Flood Hazard Areas (SFHA), Zones A, A1-30, AE.

      - Residential Construction.

All new construction, substantial improvements, and repair to structures that have sustained substantial damage which are residential structures shall have the bottom of the lowest floor, including basement, elevated one (1.0) foot above the base flood elevation (BFE).  Electrical, plumbing, machinery or other utility equipment that service the structure must be elevated one (1.0) foot above the BFE.

      - Non-Residential Construction.

All new construction, substantial improvements, and repair to structures that                have sustained substantial damage which are commercial, industrial or non-                 residential structures shall:

(a) Have the bottom of the lowest floor, including basement, elevated one (1.0) foot         above the base flood elevation (BFE); or

(b) In lieu of being elevated, non-residential structures may be dry flood-proofed        to one (1.0) foot above the BFE provided that together with all attendant utilities      and sanitary facilities the areas of the structure below the required elevation are      watertight with walls substantially impermeable to the passage of water, and            provided that such structures are composed of structural components having the      capability of resisting hydrostatic and hydrodynamic loads and the effects of            buoyancy.  A registered professional engineer or architect shall review and/or          develop structural design specifications and plans for the construction, and shall      certify that the design and methods of construction are in accordance with                acceptable standards of practice for meeting the provisions of this section.  Such      certification shall be provided to the [title of local administrator] on the FEMA        Floodproofing Certificate, Form 81-65.

(c) The bottom of all electrical, plumbing, machinery or other utility equipment              that service the structure must be elevated one (1.0) foot above the BFE.

      - Fully Enclosed Areas Below The Base Flood Elevation Of Elevated Buildings.

All new construction, substantial improvements, or repair to structures that have sustained substantial damage, whether residential or non-residential, that include fully enclosed areas formed by a foundation and other exterior walls shall have the lowest floor elevated to one (1.0) foot above the base flood elevation (BFE).  The elevated building shall be designed to preclude finished living space below the lowest floor and be designed to allow for the entry and exit of flood waters to automatically equalize hydrostatic flood forces on exterior walls (wet flood-proofing).  Designs for complying with this requirement must either be certified by a registered professional engineer or architect as meeting the requirements of ASCE 24 Section 2.6.2.2, or meet the following minimum criteria listed in sections (a)-(h) below:

(a) Provide a minimum of two (2) openings (hydraulic flood vents) having a total               net area of not less than one square inch for every one square foot of enclosed               area subject to flooding.  The enclosed area is measured on the exterior of the               enclosure walls.  These hydraulic openings must be located on at least two                     different exterior walls of each enclosed area.  If the structure has more than                one enclosed area, openings must be installed in the exterior walls of each                      enclosed area so that flood waters can enter directly from the outside;

(b) The bottom of all openings shall be no higher than one (1.0) foot above the                                          higher of either the final interior grade or floor elevation, or the finished                                             exterior grade adjacent to the outside of the foundation wall.  At least one side                                    of the structure’s fully enclosed area must be at or above grade.  Fill                                                    placed around the foundation walls must be graded so that the elevation inside                                   the enclosed area is equal to or higher than the adjacent outside elevation on at                                   least one side of the building.  The finished floor of the enclosed area shall be                                      no lower than the bottom of the foundation openings.  The foundation slab of a                                   residential structure, including the slab or a crawlspace, must be set equal to                                      the outside finished grade on at least one side of the building;

(c) The openings may be equipped with screens, louvers, valves or other coverings              or devices provided they permit the automatic entry and exit of flood waters in              both directions without any external influence or control such as human                        intervention, including the use of electrical and other non-automatic                               mechanical means.  These coverings must not block or impede the automatic                 flow of floodwaters into and out of the enclosed area.  Other coverings may be             designed and certified by a registered professional engineer or approved by the             [title of local administrator];

(d) Openings shall not be less than three (3) inches in any direction in the plane of                                     the wall;

(e) The area cannot be used as finished living space.  Use of the enclosed area shall                                   be the minimum necessary and shall only be used for the parking of vehicles,                                      building access or limited storage.  Access to the enclosed area shall be the                                           minimum necessary to allow for the parking of vehicles (garage door) or limited                                 storage of maintenance equipment used in connection with the premises                                             (standard exterior door) or entry to the living area (stairway or elevator).  The                                   enclosed area shall not be used for human habitation;

(f) All interior walls, floor, and ceiling materials located below one (1.0) foot above           the BFE shall be unfinished and resistant to flood damage-resistant in                            accordance with FEMA Technical Bulletin 2, Flood Damage-Resistant                          Requirements.

(g) Electrical, plumbing, HVAC ductwork, machinery or other utility equipment                                     and connections that service the structure (including, but not limited to,                                               furnaces, oil or propane tanks, air conditioners, heat pumps, hot water heaters,                                  ventilation, washers and dryer hook-ups, electrical junction boxes, circuit                                            breaker boxes and food freezers) are prohibited in the fully enclosed area below                                 the BFE plus one (1.0) foot.  Utilities or service equipment located in this                                            enclosed area, even if elevated one (1.0) foot above the BFE in the space, will                                       subject the structure to increased flood insurance rates.

(h) A residential building with a structurally attached garage having the floor slab                                   below the BFE is considered an enclosed area below the BFE and must meet the                                 	standards of Sections 5.3.1.3 (a)-(g).  A garage attached to a residential                                                structure, constructed with the garage floor slab below the BFE, must be                                            designed to allow for the automatic entry and exit of floodwaters in both                                             directions.  Flood openings or vents are required in the exterior walls of the                                        garage or in the garage doors.  Garage doors that must be manually opened do                                   not meet the flood vent opening requirements in Section 5.3.1.3 (a)-(c).  In                                           addition to the automatic entry of floodwaters, the areas of the garage below                                       BFE plus one (1.0) foot must be constructed with flood damage-resistant                                             materials per the requirements of FEMA Technical Bulletin 2.  Garages                                              attached to non-residential structures must also meet the aforementioned                                            requirements or be dry floodproofed as per the requirements of Section 5.3.1.2.

    - Manufactured (Mobile) Homes and Recreational Vehicles (RVs).

      - In all Special Flood Hazard Areas (SFHA), any manufactured (mobile) homes to be      newly placed, undergoing a substantial improvement or repaired as a result of substantial damage, shall be elevated so that the bottom of the frame is located one (1.0) foot above the base flood elevation (BFE).  The manufactured home must also meet all the construction standards per Section 5.3.1.  The foundation and anchorage of manufactured homes to be located in floodways shall be designed and constructed in accordance with ASCE24.  This includes SFHAs outside a manufactured home park or subdivision, in a new manufactured home park or subdivision, in an existing manufactured home park or subdivision, in an expansion to an existing manufactured home park or subdivision, or on a site in an existing park which a manufactured home has incurred substantial damage as a result of a flood.

5.3.2.2   All manufactured (mobile) homes within a SFHA shall be placed on a permanent                                       foundation which itself is securely anchored and to which the structure is securely                                     anchored so that it will resist flotation, lateral movement and hydrostatic pressures.                                    Anchoring may include, but not be limited to, the use of over-the-top or frame ties                                     to ground anchors.

5.3.2.3  All manufactured (mobile) homes within a SFHA shall be installed using methods and                                practices which minimize flood damage.  Adequate access and drainage should be                                      provided.  Elevation construction standards include piling foundations placed no                                        more than ten (10) feet apart, and reinforcement is provided for piers more than six                                    (6) feet above ground level.

5.3.2.4  Recreational vehicles placed on sites within a SFHA shall either (i) be on the site for              		       fewer than 180 consecutive days, and (ii) be fully licensed and ready for highway use,                               OR (iii) meet all the general standards of Section 5.1 and the elevation and anchoring                   	        requirement of Section 5.3.2.1, 5.3.2.2, and 5.3.2.3.  A recreational vehicle is ready              		        for highway use if it is on its wheels or jacking system, is attached to the site only                		        by quick disconnect type utilities and security devices, and has no permanently                                           attached additions.

    - Floodways

Located within Special Flood Hazard Areas (SFHA) are areas designated as floodways on the community’s Flood Insurance Rate Maps (FIRM) or Flood Boundary and Floodway Maps (FBFM).  Since the floodway is an extremely hazardous area due to the velocity of flood waters which carry debris, potential projectiles and has erosion potential, no encroachments, including fill, new construction, substantial improvements, repairs to substantially damaged structures and other developments shall be permitted unless certification, with supporting technical data, by a registered professional engineer is provided demonstrating, through hydrologic and hydraulic analyses performed in accordance with standard engineering practice, that encroachments shall not result in any (0.00 feet) increase in flood levels during occurrence of the base flood discharge published by FEMA.  Buildings and structures meeting the standard above and located in whole or in part in the floodway shall be designed and constructed in accordance with ASCE 24.  Fences in the floodway must be aligned with the flow and be of an open design.  A permit may be given which allows encroachments resulting in increases in base flood elevations provided the community first obtains a conditional floodway revision by meeting the requirements of C.F.R. 44, Chapter 1, Subsection 65.12.

    - Standards for Development in Areas of Shallow Flooding (Zones AO and AH)

Located within the Special Flood Hazard Areas (SFHA) are areas designated as shallow flooding areas (AO and AH Zones).  These areas have flood hazards associated with base flood depths of one (1) to three (3) feet where a clearly defined channel does not exist and where the path of flooding is unpredictable and indeterminate.  In AO and AH zones, the following provisions apply:

5.3.4.1  For residential structures, all new construction, substantial improvements and                            repair to structures that have sustained substantial damage shall have the lowest

floor, including basement, elevated above the highest adjacent grade at least as                   high as one (1.0) foot above the depth number specified on the Flood Insurance                   Rate Map (FIRM.  If no depth number is specified, the lowest floor, including                    basement, shall be elevated at least three (3.0) feet above the highest adjacent                     grade.

      - For non-residential structures, all new construction, substantial improvements and repair to structures that have sustained substantial damage shall:

- Have the lowest floor, including basement, elevated above the highest adjacent grade at least as high as one (1.0) foot above the depth number specified on the Flood Insurance Rate Map (FIRM). If no depth number is specified, the lowest floor, including basement, shall be elevated at least three (3.0) feet above the highest adjacent grade; or

(b) Together with attendant utility and sanitary facilities be completely flood-                                            proofed to above the highest adjacent grade at least as high as one (1.0)                                               foot above the depth number specified on the FIRM, or if no depth                                                       number is specified at least three (3.0) feet above the highest adjacent                                                  grade, so that any space below that level is watertight with walls substantially                                            impermeable to the passage of water and with structural components having                                               the capability of resisting hydrostatic and hydrodynamic loads and effects of                                              buoyancy.  Designs for complying with this requirement must be certified by                                              either a registered professional engineer or architect.

      - On-site drainage for all proposed structures in AO and AH Zones located on           slopes shall provide adequate drainage paths to guide flood waters around and        away from such structures.

      - Fully enclosed areas below the lowest floor in AO and AH Zones must comply with the provisions of Section 5.3.1.3 for hydraulic flood vents.

# DESIGN STANDARDS FOR SUBDIVISION PROPOSALS

# If a proposed subdivision, including the placement of a manufactured home park or subdivision, is located in a Special Flood Hazard Area (SFHA) the following requirements shall apply:

# 6.1  All subdivision proposals shall be consistent with the need to minimize flood damage;

# 6.2  All subdivision proposals shall have public utilities and facilities such as sewer, gas, electrical        and water systems located and constructed to minimize flood damage;

# All subdivision proposals shall have adequate drainage provided to reduce exposure to flood hazards; and

# The [title of local administrator] shall require the applicant to provide BFE data for all subdivision proposals, including manufactured home parks and subdivisions, as per Section 4.5.12.  In all special flood hazard areas where base flood elevation (BFE) data is not available, the applicant shall provide a hydrologic and hydraulic engineering analysis performed by a registered professional engineer that generates BFEs for all subdivision proposals and other proposed development, including manufactured home parks and subdivisions.

7.0  	VARIANCE PROCEDURES

7.1	ESTABLISHMENT OF VARIANCE PROCESS

7.1.1	The [local appeal board], as established by the [Municipality], shall hear and decide

appeals and requests for variances from the requirements of this [ordinance/regulation].

    - The [local appeal board] shall hear and decide appeals when it is alleged there is an

error in any requirement, decision or determination made by the [title of local                                            administrator] in the enforcement or administration of this [ordinance/regulation].

    - Any person aggrieved by the decision of the [local appeal board] or any person

owning land which abuts or is within a radius of one hundred (100) feet of the land in                                question may appeal within fifteen (15) days after such decision to the State Superior Court                      of [Judicial District], as provided in Section 8-8 of the General Statutes of Connecticut.

    - The [local administrator] shall maintain the records of all appeal actions and report any

variances to the Federal Emergency Management Agency (FEMA) in its biennial report.

7.2	SPECIFIC SITUATION VARIANCES

7.2.1	Buildings on a Historic Register

Variances may be issued for the reconstruction, rehabilitation or restoration of structures                           listed on the National Register of Historic Places, the State Inventory of Historic Places, or                       any locally-adopted historic district without regard to the procedures set forth in the                                   remainder of this section and provided the proposed reconstruction, rehabilitation or                                  restoration will not result in the structure losing its historical designation.

    - Functionally Dependent Use or Facility

Variances may be issued for new construction and substantial improvements and other development necessary for the conduct of a functionally dependent use or facility         provided the structure or other development is protected by methods that minimize flood damage, creates no additional threat to public safety and meet all the requirements of Section 7.4.

    - Floodway Prohibition

Variances shall not be issued within any designated floodway if any increase in                    flood levels during the base flood discharge would result.

7.3 	CONSIDERATIONS FOR GRANTING OF VARIANCES

In passing upon such applications, the [local appeal board] shall consider all technical        evaluations, all relevant factors, all standards specified in other sections of this [ordinance/regulation] and the items listed below as 7.3.1 – 7.3.11. Upon consideration of these factors and the purposes of this [ordinance/regulation], the [local appeal board] may attach such conditions to the granting of variances as it deems necessary to further the purposes of this [ordinance/regulation].

    - The danger that materials may be swept onto other lands to the injury of others;

    - The danger to life and property due to flooding or erosion damage;

7.3.3   The susceptibility of the proposed facility and its contents to flood damage and the                                     effect of such damage on the individual owner;

7.3.4   The importance of the services provided by the proposed facility to the community;

7.3.5  The necessity of the facility to waterfront location, in the case of a functionally dependent               facility;

    - The availability of alternative locations not subject to flooding or erosion damage for the

proposed use;

    - The compatibility of the proposed use with existing and anticipated development;

    - The relationship of the proposed use to the comprehensive plan and floodplain management program for that area;

    - The safety access to the property in times of flood for ordinary and emergency vehicles;

7.3.10	 The expected heights, velocity, duration, rate of rise and sediment transport of the                                      flood waters and the effects of wave action, if applicable, expected at the site; and

7.3.11	The costs of providing governmental services during and after flood conditions                                    including maintenance and repair of public utilities and facilities such as sewer,

gas, electrical and water systems, and streets and bridges.

7.4    CONDITIONS FOR VARIANCES

7.4.1	Variances shall only be used upon a determination that the variance is the minimum necessary to afford relief considering the flood hazard; and in the instance of a historical building, a determination that the variance is the minimum necessary as not to destroy the historic character and design of the building and result in the loss of historic designation of the building.  Variances pertain to a piece of property and are not personal in nature.  A properly issued variance is granted for a parcel of property with physical characteristics so unusual that complying with the regulation would create an exceptional hardship to the applicant or the surrounding property owners.  Those characteristics must be unique to that property and not be shared by adjacent parcels.  For example, economic or financial hardship is not sufficient cause for a variance, nor are inconvenience, aesthetic considerations, physical handicaps, personal preferences or disapproval of one’s neighbors.

    - Variances shall only be used upon (i) a showing of good and sufficient cause, (ii) a

determination that failure to grant the variance would result in exceptional hardship, and; (iii) a determination that the granting of a variance will not result in increased flood heights, additional threats to public safety, extraordinary public expense, create nuisance, damage the rights or property values of other persons in the area, cause fraud on or victimization of the public, or conflict with existing local laws, ordinances or regulations.  Only hardships that are based on unusual or unique physical characteristics of the property in question, characteristics that are not shared by adjacent parcels, shall quality to meet subsection (ii) above.  Claims of hardship based on the structure, on economic gain or loss, or on personal or self-created circumstances are not sufficient cause for the granting of a variance.

    - No variance may be issued within a regulatory floodway that will result in any increase in

the 100-year flood levels.  A variance may be issued for new construction, substantial improvements and other development necessary for the conduct of a “functionally dependent use” provided that there is good and sufficient cause for providing relief; and the variance does not cause a rise in the 100-year flood level within a regulatory floodway.  The structure and other development must be protected by methods that minimize flood damages.

7.4.4  Any applicant to whom a variance is granted shall be given written notice that the structure             will be permitted to be built with the lowest floor elevation below the base flood elevation             (BFE), and that the cost of flood insurance will be commensurate with the increased risk                resulting from the lowest floor elevation up to amounts as high as $25 for $100 of insurance            coverage.

# 8.0	ENFORCEMENT

8.1	Each [Floodplain/Development/Building/Zoning] Permit shall authorize, as a condition of approval, the [title of local administrator] or designated agents to make regular inspections of the subject property.  The [title of local administrator] or designated agents are also authorized to inspect any property in a Special Flood Hazard Area (SFHA) where it appears that violations of these regulations may be taking place.

8.2    If the [title of local administrator] finds that any person is undertaking any construction,              substantial improvement, filling, or any other activity or maintaining a condition which in              violation of these regulations, the [title of local administrator] shall:

    - Issue a written order by certified mail, return receipt requested, to the subject

property owner, ordering that the activity cease and ordering the property owner to                                    either seed to obtain a [Floodplain Development/Building/Zoning] Permit prior to                                    continuing with the activity or, if appropriate, ordering that all violations and/or                                         obstructions be removed from the Special Flood Hazard Area (SFHA) immediately.

    - Notify the [Building Official/Inspector] and request that any

[floodplain/building/zoning/development] permit(s) in force be revoked or                        suspended and that a stop work order be issued.

    - The [title of local administrator] may suspend or revoke a Floodplain Development Permit if it is found that the applicant has not complied with the terms, conditions or limitations set forth in the permit or has exceeded the scope of work as set forth in the application including application plans.  Prior to revoking any permit, the [title of local administrator] shall issue notice to the permittee, personally or by certified mail, return receipt requested, setting forth the facts or conduct which warrants the intended action.

    - Failure to comply with any written order issued under this section shall be

considered a violation of these regulations and is subject to the penalties described in            Section 10.0.

    - In the event violations or obstructions are not promptly removed from the Special

Flood Hazard Area (SFHA), the [title of local administrator] may cause such                      removal and remediation work to be performed utilizing bond money held in escrow            pursuant to Section 3.0 of this [ordinance/regulation], or may direct the [director              of public works or appropriate agent] to cause such work to be done and to place             a lien against the property.

    - Any person subjected to enforcement action pursuant to this

[ordinance/regulation], may appeal any requirement, decision, or determination of             the [title of local administrator] to the [local appeals board], in accordance with              Section 6.0 of this [ordinance/regulation].  Such person shall provide such                          information as necessary including appropriate certifications from a registered                      professional engineer or architect in order to substantiate the claim that the                           requirement, decision, or determination of the [title of local administrator] was in              error or unwarranted.

9.0	PENALTIES FOR VIOLATION

Any violation of the provisions of this [ordinance/regulation] or failure to comply with any of its requirements, including violation of conditions and safeguards established in connection with grant of variances or special exceptions, shall constitute a misdemeanor.  Any person who violates this [ordinance/regulation] or fails to comply with any of its requirements shall, upon conviction thereof, be fined a penalty of [$250.00] per day [or imprisoned for not more than ten (10) days for each day of violation, or both,] and in addition shall pay all costs and reasonable legal fees involved in the case.  Nothing herein contained shall prevent the [Municipality] from taking such lawful action as is necessary to prevent or remedy any violation.